## Slide 1: ISE tutorial
柏宏

## Slide 2: Download
website: https://www.xilinx.com/support/download/index.html/content/xilinx/en/downloadNav/vivado-design-tools/archive-ise.html
14.7 win10 version: base on VM
If you are lazy, you can choose these
Download
-> Win 10 has bugs need to fix

## Slide 3: Install ISE 14.7

## Slide 4: Install ISE 14.7
Choose ISE WebPack (free) Edition

## Slide 5: Get Free license
Choose ‘Get Free ISE WebPack License’ and ‘click Connect Now’

## Slide 6: Get Free license
Sign in & fill out verification form

## Slide 7: Get Free license
1
2
3
4
License will send to your mail

## Slide 8: Activate License
Download file from mail
1
2
3
4
5. Close Xilinx License Configuration Manager

## Slide 9: WAIT! Fix bug if using win10
Bug : Crash of ISE
Solution:
  In path: C:\Xilinx\14.7\ISE_DS\ISE\lib\nt64
  Rename file ‘libPortability.dll’ as ‘libPortability_original.dll’
  Rename file ‘libPortabilityNOSH.dll’ as ‘libPortability.dll’

## Slide 10: Create new project
Select New Project... or File -> New Project…

## Slide 11: Create new project
Select Next

## Slide 12: Create new project
Select Device & Specify Project property
Project summary page

## Slide 13: Linear Feedback Shift Register
Ref.: Lecture 6: A Random Number Generator in Verilog
XOR + D-Flip flop + MUX

## Slide 14: Create Verilog Module File
Choose Verilog module and assign file name as mux_2to1

## Slide 15: Create 2 to 1 Mux

## Slide 16: Modify file mux_2to1.v
module mux_2to1(
input sel,
input input_A,
input input_B,
output reg output_Z
);
always@(*)begin
if(!sel) begin//sel=0 output_Z=input_A
output_Z = input_A;
end
else begin//sel=1 output_Z=input_B
output_Z = input_B;
end
end
endmodule
Modify and save

## Slide 17: Add Files to Project
Select Project -> Add Source
Select Add Source icon on left-side menu bar
Push right mouse button to select Add Source

## Slide 18: Add Files to Project
Select Project -> Add Source
Select Add Source icon on left-side menu bar
Push right mouse button to select Add Source
Those files are provided by TA

## Slide 19: After add file

## Slide 20: Compile Program
Compile program

## Slide 21: Create test bench source
Add new source -> Verilog Text Fixture (testbench file)

## Slide 22: Select source you want to test
Now we want to test lfsr, so choose it

## Slide 23: After create test bench
Choose simulation
Double click lfsr_tb

## Slide 24: Modify test bench
Copy and paste the code
initial begin
reset = 0;
#10 reset = 1; // reset pulse
#10 reset = 0;
end
initial clk = 0;
always #50 clk = !clk; // generate clock
initial begin
load = 0;
seed = 0;
#100 seed = 4'b0001;
load = 1;
#100 load = 0;
end
initial #2000 $finish;
initial $monitor($realtime,"ns %h %h %h\n",load,seed,result);
endmodule
`timescale 1ns / 1ps
module lfsr_tb;
// Inputs
reg clk;
reg reset;
reg load;
reg [3:0] seed;
// Outputs
wire [3:0] result;
// Instantiate the Unit Under Test (UUT)
lfsr uut (
.clk(clk),
.reset(reset),
.load(load),
.seed(seed),
.result(result)
);

## Slide 25: Check syntax and Simulate
Behavioral Check syntax
  check syntax of test bench
Simulate Behavior Model
  generate wave

## Slide 26: ISIM
After double click Simulate Behavior Mode -> get the wave
Click to run all

## Slide 27: Lab0 part 1
Please change radix of result to Unsigned Decimal
Take screenshot of wave to the report
這個作業很簡單,請把result換成10進制無號數,並截圖放到report.